Lr.No.;SKU/Engg/A1/Providing Lift in Central Library/2023)

QUOTATIONS:

25-08-2023:  Sealed Quotations are invited from reputed firms  for Providing  Lift in Central Library on or before 2nd  September 2023 in a sealed cover by Register  Post / Courier.

| S.No. | Description | per | Rate |
| --- | --- | --- | --- |
| 1. | Type | Passenger (6 Passengers) | 1Unit |  |
| 2. | Load & Speed | 408 Kgs & 0.63m/second |  |  |
| 3. | Controller | Micro Processor (With Auto Reset System) |  |  |
| 4. | Power supply | 415 Volts, 3Phase, 50 Cycles A.C G+1 |  |  |
| 5. | Travel | G+1 |  |  |
| 6. | Stops & Openings machine | 2 stops & 2 Openings Directly Placed above the Hoistway Montanari Machine |  |  |
| 7. | Operation | VVVF Drive MD 500 LT GBO Fuji/Monarch Drive |  |  |
| 8. | Hoistway Required | 1660x1500 (Width & Depth) |  |  |
| 9. | Available Car size | 1200 x1100 (width & Depth) |  |  |
| 10. | Car Enclosure | S.S 304 Hair Lane Finish, 1.2 Thickness, 18 Finish Cabin with Fan, Light, Door Open Announcer & Emergency Hooter |  |  |
| 11 | Car Entrance | Protected By S.S. Auto Doors |  |  |
| 12. | Hoistway Entrances | Protected by S.S. Auto Doors |  |  |
| 13. | Hand Rail | Stainless steel Round hand rail located rear side of the cabin |  |  |
| 14. | LOP Location | Landing display on wall and in Stainless steel cabin |  |  |
| 15. | Door Type | Automatic fully Sensor, centre opening sliding door of size 800 x2000 mm |  |  |
| 16. | Rope Make | Usha Martin (8x19S) Self Lubricated |  |  |
| 17. | Time for completion of work | 1 Month |  |  |

- The quotations should be in the name of “The Registrar,                      S.K. University, Ananthapuramu- 515003, Andhra Pradesh.

- The Last date for quotation to reach “The Superintending Engineer, S.K. University, Ananthapuramu- 515003, Andhra Pradesh.”on or before 02-09-2023, 5:00 P.M.